## Slide 1: Current and Potential Future Supply and Demand in Santa Cruz
Water Supply Advisory Committee
June 26-27, 2014

## Slide 2: Presentation Overview
Introduction and Context
A Representational View of How Sources are Deployed to Meet Demand
Current Supply
Current Demand
Future Supply
Future Demand
Conclusions and Take Aways

## Slide 3: Introduction and Context
The fundamental question the WSAC will have to grapple with in its work is the reliability of Santa Cruz’s water supply.
The fundamental measure for reliability is the degree to which available supply can meet existing and future demand under a range of foreseeable and unforeseeable but probable circumstances or conditions.

## Slide 4: How Water Sources are Deployed to Meet Demand
A Representational View

## Slide 5: Average Monthly System Demand
Millions of Gallons per Day

## Slide 6: Supply and Demand in Average Conditions
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North Coast | 3 | 3.8 | 4.3 | 4 | 3.5 | 3 | 2.5 | 2.2 | 2 | 1.9 | 1.8 | 2.4
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7

North Coast
Millions of Gallons per Day

## Slide 7: Supply and Demand in Average Conditions
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North Coast | 3 | 3.8 | 4.3 | 4 | 3.5 | 3 | 2.5 | 2.2 | 2 | 1.9 | 1.8 | 2.4
San Lorenzo River | 4.1 | 3.6 | 3.7 | 5.9 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.2 | 4.6
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7

North Coast
San Lorenzo River
Millions of Gallons per Day

## Slide 8: Supply and Demand in Average Conditions
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North Coast | 3 | 3.8 | 4.3 | 4 | 3.5 | 3 | 2.5 | 2.2 | 2 | 1.9 | 1.8 | 2.4
San Lorenzo River | 4.1 | 3.6 | 3.7 | 5.9 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.2 | 4.6
Beltz | 0 | 0 | 0 | 0 | 0.2 | 0.8 | 0.8 | 0.8 | 0.8 | 0.6 | 0 | 0
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7
San Lorenzo River
North Coast
Live Oak Wells
Millions of Gallons per Day

## Slide 9: Supply and Demand in Average Conditions
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North Coast | 3 | 3.8 | 4.3 | 4 | 3.5 | 3 | 2.5 | 2.2 | 2 | 1.9 | 1.8 | 2.4
San Lorenzo River | 4.1 | 3.6 | 3.7 | 5.9 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.2 | 4.6
Beltz | 0 | 0 | 0 | 0 | 0.2 | 0.8 | 0.8 | 0.8 | 0.8 | 0.6 | 0 | 0
Loch Lomond | 0 | 0 | 0 | 0 | 0 | 0.7 | 1.4 | 1.5 | 0.7 | 0 | 0 | 0
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7
North Coast
San Lorenzo River
Live Oak Wells
Loch Lomond Reservoir
Millions of Gallons per Day

## Slide 10: Supply and Demand in a Drought
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7


Millions of Gallons per Day

## Slide 11: Supply and Demand in a Drought
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North Coast | 1.5 | 1.9 | 2.2 | 2 | 1.7 | 1.5 | 1.2 | 1.1 | 1 | 0.9 | 0.9 | 1.2
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7

North Coast
Millions of Gallons per Day

## Slide 12: Supply and Demand in a Drought
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North Coast | 1.5 | 1.9 | 2.2 | 2 | 1.7 | 1.5 | 1.2 | 1.1 | 1 | 0.9 | 0.9 | 1.2
San Lorenzo River | 5.5 | 5.5 | 5.8 | 7.5 | 7.5 | 7 | 6.5 | 6 | 5.5 | 5 | 5.5 | 5.8
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7

North Coast
San Lorenzo River
Millions of Gallons per Day

## Slide 13: Supply and Demand in a Drought
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North Coast | 1.5 | 1.9 | 2.2 | 2 | 1.7 | 1.5 | 1.2 | 1.1 | 1 | 0.9 | 0.9 | 1.2
San Lorenzo River | 5.5 | 5.5 | 5.8 | 7.5 | 7.5 | 7 | 6.5 | 6 | 5.5 | 5 | 5.5 | 5.8
Beltz | 0 | 0 | 0 | 0 | 0.2 | 0.8 | 0.8 | 0.8 | 0.8 | 0.6 | 0 | 0
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7
North Coast
San Lorenzo River
Live Oak Wells
Millions of Gallons per Day

## Slide 14: Supply and Demand in a Drought
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North Coast | 1.5 | 1.9 | 2.2 | 2 | 1.7 | 1.5 | 1.2 | 1.1 | 1 | 0.9 | 0.9 | 1.2
San Lorenzo River | 5.5 | 5.5 | 5.8 | 7.5 | 7.5 | 7 | 6.5 | 6 | 5.5 | 5 | 5.5 | 5.8
Beltz | 0 | 0 | 0 | 0 | 0.2 | 0.8 | 0.8 | 0.8 | 0.8 | 0.6 | 0 | 0
Loch Lomond | 0 | 0 | 0 | 0.4 | 1.2 | 1.3 | 2 | 1.8 | 1.5 | 1 | 0.6 | 0
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7
North Coast
San Lorenzo River
Live Oak Wells
Loch Lomond Reservoir
Millions of Gallons per Day

## Slide 15: Supply and Demand in a Drought
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North Coast | 1.5 | 1.9 | 2.2 | 2 | 1.7 | 1.5 | 1.2 | 1.1 | 1 | 0.9 | 0.9 | 1.2
San Lorenzo River | 5.5 | 5.5 | 5.8 | 7.5 | 7.5 | 7 | 6.5 | 6 | 5.5 | 5 | 5.5 | 5.8
Beltz | 0 | 0 | 0 | 0 | 0.2 | 0.8 | 0.8 | 0.8 | 0.8 | 0.6 | 0 | 0
Loch Lomond | 0 | 0 | 0 | 0.4 | 1.2 | 1.3 | 2 | 1.8 | 1.5 | 1 | 0.6 | 0
Deficit | 0 | 0 | 0 | 0 | 0.6 | 1.4 | 1.7 | 2.3 | 2.2 | 2.5 | 2 | 0
Demand | 7.1 | 7.4 | 8 | 9.9 | 11.2 | 12 | 12.2 | 12 | 11 | 10 | 9 | 7
North Coast
San Lorenzo River
Live Oak Wells
Loch Lomond Reservoir
Deficit
Millions of Gallons per Day

## Slide 16: The Role of Curtailment

## Slide 17: Curtailment is a strategy used to respond to short term supply deficiencies
The 2009 Water Shortage Contingency Plan, sets the following overarching goals:
  To conserve the water supply of the City for the greatest public benefit;
  To mitigate the effects of a water supply shortage on public health and safety, economic activity, and customers lifestyle; and
  To budget water use so that supply will be available for the most essential purposes for the entire duration of the water shortage.

## Slide 18: The Water Shortage Contingency Plan Uses a Priority-Based Allocation System
When a shortage occurs, available water supply is classified into 3 usage priorities:
Priority | Type of Water Use
Highest | Health and safety: Indoor domestic use for personal care
Next highest | Business (protect jobs/economy)
Lowest | Landscape, yard, or garden irrigation and other outdoor uses

## Slide 19
 | No Deficiency |  | Stage 2 15% Deficiency |  | Stage 3 25% Deficiency |  | Stage 4 35% Deficiency |  | Stage 5 50% Deficiency | 
 | Delivery |  | Delivery |  | Delivery |  | Delivery |  | Delivery | 
Normal Peak Season Demand = 2,473 mil gal | % | Volume (mil gal) | % | Volume (mil gal) | % | Volume (mil gal) | % | Volume (mil gal) | % | Volume (mil gal)
Single Family Residential | 100 | 1,031 | 84% | 864 | 73% | 753 | 62% | 639 | 48% | 495
Multiple Residential | 100 | 524 | 87% | 454 | 78% | 411 | 69% | 361 | 55% | 287
Business | 100 | 438 | 95% | 416 | 92% | 402 | 87% | 381 | 70% | 307
UC Santa Cruz | 100 | 132 | 85% | 113 | 76% | 100 | 66% | 87 | 52% | 68
Other Industrial | 100 | 23 | 95% | 22 | 90% | 21 | 85% | 20 | 67% | 15
Municipal | 100 | 48 | 76% | 36 | 57% | 27 | 41% | 20 | 28% | 14
Irrigation | 100 | 110 | 64% | 70 | 34% | 37 | 12% | 13 | 0% | 0
Golf Course Irrigation | 100 | 106 | 73% | 78 | 51% | 54 | 34% | 36 | 20% | 21
Coast Agriculture | 100 | 59 | 95% | 56 | 90% | 53 | 85% | 50 | 67% | 40
Other | 100 | 2 | 95% | 2 | 90% | 2 | 50% | 1 | 50% | 1
Total | 100 | 2,473 | 85% | 2,111 | 75% | 1,861 | 65% | 1,607 | 50% | 1,247
Demand Reduction %, Million gallons | 0 | 0 | 15% | -362 | 25% | -612 | 35% | -866 | 50% | -1,226
Table ES-3. Water Supply Allocation and Customer Reduction Goals

## Slide 20: Current Supply

## Slide 21
Beltz Wells
4%
Tait Wells
3%
Loch
Lomond
22%
San Lorenzo
River
46%
North Coast
Streams
25%
North Coast Streams (1890)
Loch Lomond Reservoir (1960)
San Lorenzo River (1924)
Beltz Wells (1964)
Water Sources

## Slide 22: City of Santa Cruz Water Rights

## Slide 23: Gross Water Supply Sources for the City of Santa Cruz’s Water Utility, 2009-2013
 | Calendar Year All figures in million of gallons |  |  |  | 
Source | 2009 | 2010 | 2011 | 2012 | 2013
Coastal Sources | 814 | 1,168 | 1,211 | 711 | 400
San Lorenzo River | 2,038 | 1,468 | 1,465 | 1,959 | 2,110
Loch Lomond | 195 | 411 | 228 | 462 | 807
Beltz Wells | 165 | 145 | 163 | 163 | 160
Totals | 3,212 | 3,192 | 3,067 | 3,295 | 3,477

## Slide 24: Annual runoff from the San Lorenzo River is highly variable 1 acre foot = 325,851.427 gallons

## Slide 25
Annual Production by Source
Chart: Water Year
| 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
San Lorenzo River | 1341.201 | 423.569 | 569.035 | 943.789 | 1974.951 | 1807.277 | 782.104 | 1091.471 | 1157.411 | 1660.912 | 1103.704 | 770.257 | 745.447 | 1826.978 | 1683.332 | 2361.336 | 2116.444 | 1940.416 | 2141.416 | 2046.091 | 1787.606 | 1656.209 | 1904.85 | 1314.255 | 1327.909 | 1661.769 | 1402.423 | 2108.841 | 1981.302 | 2240.263 | 1851.374 | 1944.209 | 2039.791 | 1506.759 | 1572.133 | 2258.833 | 2138.348 | 2010.489 | 1631.016 | 1360.02 | 1988.089 | 2007.005
Loch Lomond | 749.973 | 1026.93 | 1324.581 | 1508.31 | 644.572 | 164.763 | 932.674 | 1116.44 | 1048.633 | 903.768 | 787.26 | 1329.987 | 1542.672 | 835.983 | 1205.555 | 939.44 | 717.839 | 474.637 | 220.098 | 435.175 | 677.005 | 935.369 | 861.791 | 971.737 | 1228.461 | 1296.498 | 1251.343 | 476.819 | 846.289 | 736.595 | 585.184 | 711.385 | 698.738 | 616.045 | 537.245 | 445.653 | 470.792 | 295.995 | 314.98 | 336.057 | 296.94 | 813.128
Laguna Creek | 221.302 | 794.517 | 794.4 | 482.392 | 157.359 | 73.357 | 691.892 | 548.43 | 691.475 | 356.525 | 809.77 | 694.356 | 595.817 | 427.534 | 584.373 | 249.631 | 204.797 | 270.966 | 333.125 | 297.757 | 249.453 | 447.541 | 299.6996 | 619.941 | 737.011 | 755.606 | 890.075 | 929.827 | 776.561 | 555.841 | 723.7191 | 552.011 | 606.17 | 863.943 | 974.792 | 374.144 | 332.112 | 243.945 | 584.991 | 741.855 | 247.176 | 72.129
Liddel Spring | 405.348 | 466.327 | 496.053 | 480.268 | 412.61 | 317.918 | 293.209 | 378.767 | 429.512 | 338.063 | 397.543 | 388.851 | 433.224 | 416.169 | 417.103 | 372.702 | 325.893 | 363.517 | 342.602 | 302.02 | 284.982 | 276.1 | 273.518 | 326.739 | 481.21 | 439.118 | 457.005 | 521.679 | 543.905 | 507.468 | 525.97 | 495.664 | 506.784 | 467.246 | 580.049 | 447.993 | 411.34 | 380.882 | 389.538 | 417.276 | 354.091 | 264.245
Tait Wells | 439.256 | 453.095 | 210.962 | 5.027 | 266.805 | 134.706 | 63.275 | 0 | 0 | 226.452 | 135.533 | 155.091 | 161.503 | 268.783 | 133.194 | 116.233 | 274.604 | 281.631 | 148.738 | 195.956 | 257.921 | 79.736 | 263.379 | 238.74 | 73.569 | 5.153 | 1.732 | 76.061 | 66.39 | 67.037 | 103.503 | 31.763 | 71.624 | 47.979 | 4.658 | 108.046 | 70.105 | 110.231 | 100.229 | 53.639 | 41.441 | 35.118
Beltz Wells | 218.987 | 241.354 | 137.728 | 123.109 | 202.195 | 86.068 | 73.834 | 8.467 | 34.236 | 135.661 | 42.537 | 113.215 | 114.891 | 159.284 | 42.64 | 333.534 | 393.167 | 289.061 | 274.53 | 119.986 | 287.378 | 123.757 | 172.3 | 89.377 | 48.753 | 77.132 | 83.507 | 104.129 | 191.131 | 127.855 | 153.582 | 148.462 | 136.964 | 84.596 | 112.447 | 138.593 | 185.361 | 179.296 | 141.44 | 176.64 | 162.692 | 156.912
Majors Creek | 280.604 | 180.788 | 114.198 | 202.43 | 218.272 | 165.033 | 45.019 | 187.982 | 105.157 | 180.854 | 68.406 | 26.984 | 123.778 | 122.656 | 108.807 | 92.62 | 118.122 | 135.568 | 187.49 | 149.761 | 82.312 | 81.448 | 136.507 | 82.086 | 135.899 | 63.032 | 53.917 | 158.918 | 153.333 | 249.785 | 191.349 | 238.277 | 179.373 | 125.951 | 90.098 | 129.835 | 137.472 | 189.438 | 142.434 | 26.8 | 192.233 | 113.084

## Slide 26
Chart: Monthly Production (2012)
| January | February | March | April | May | June | July | August | September | October | November | December
San Lorenzo River | 150.21 | 161.122 | 106.138 | 121.181 | 181.24 | 219.333 | 226.874 | 224.576 | 206.999 | 168.76 | 108.182 | 84.92
Loch Lomond | 24.033 | 1.301 | 76.333 | 53.815 | 18.207 | 27.866 | 16.796 | 14.228 | 12.111 | 38.137 | 70.5 | 108.332
Laguna Creek | 11.3 | 1.51 | 12.598 | 13.28 | 14.161 | 2.894 | 34.277 | 32.014 | 29.099 | 20.92 | 16 | 18.527
Liddel Spring | 32.017 | 28.337 | 26.462 | 16.58 | 27.661 | 32.742 | 30.766 | 31.814 | 29.651 | 29.258 | 27.47 | 8.862
Tait Wells | 4.635 | 8.019 | 9.661 | 9.878 | 0.001 | 1.839 | 1.104 | 0.086 | 0.027 | 4.44 | 1.606 | 8.916
Beltz Wells | 0 | 0 | 0 | 14.635 | 30.871 | 27.218 | 23.66 | 24.473 | 22.419 | 19.416 | 0 | 0
Majors Creek | 13.393 | 18.474 | 8.913 | 6.59 | 24.607 | 23.574 | 19.917 | 17.122 | 15.803 | 21.395 | 12.583 | 0
Monthly Production by Source, 2012

## Slide 27
Chart: Water Production (million gallons/year)
| January | February | March | April | May | June | July | August | September | October | November | December
San Lorenzo River | 179.412 | 186.185 | 201.691 | 204.041 | 231.433 | 222.457 | 214.504 | 85.775 | 119.645 | 135.313 | 142.653 | 187.114
Loch Lomond | 21.726 | 4.391 | 19.55 | 35.484 | 71.057 | 51.75 | 69.495 | 188.791 | 133.915 | 122.692 | 73.51 | 14.539
Laguna Creek | 11.513 | 1.556 | 0 | 1.133 | 2.48 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Liddel Spring | 5.902 | 0.984 | 25.84 | 28.65 | 22.26 | 29.59 | 29.7 | 29.72 | 26.009 | 26.578 | 25.983 | 24.86
Tait Wells | 0.635 | 0.542 | 1.131 | 0.938 | 0.021 | 0.005 | 0.788 | 3.974 | 12.122 | 23.675 | 10.536 | 1.187
Beltz Wells | 2.907 | 17.068 | 0.01 | 0.01 | 1.638 | 29.889 | 30.885 | 30.778 | 26.91 | 19.724 | 0.009 | 0.009
Majors Creek | 4.155 | 1.745 | 5.124 | 2.876 | 9.618 | 15.322 | 13.533 | 14.284 | 12.449 | 11.703 | 9.271 | 6.93
Monthly Production by Source, 2013

## Slide 28: Short Term Flow Agreements
For several years, the Water Department has negotiated short term (6 month window) flow agreements with the California Department of Fish and Wildlife and the NOAA National Marine Fisheries Service;
The flows agreed to are designed to address the flow needs of the fish species and life stages that are relevant during that 6 month window; and
The flow agreements are specifically agreed not to be precedent setting for either party.

## Slide 29: Current Demand

## Slide 30: Why do we see so many different numbers for production and demand?
Chart: Billions of Gallons per year
| Components of Demand
Column2 | 3.041
Column3 | 0.331
Column4 | 0.105
Gross production is all the water that is taken into the system, and includes raw water sales and raw water system losses
Net Production is all the water that goes through the GHWTP + Beltz Wells and includes system uses (e.g., flushing) and losses
Metered water consumption includes potable water sales billed to customers
Calendar year 2013 data: gross production = 3.477 in billions of gallons

## Slide 31
Chart: Population, Accounts, Water Production, and Rainfall 1951-2013
Population | 3372 | 4560 | 6300 | 8100 | 9661.92 | 10343.64 | 10324.032 | 10345.944 | 10426.896 | 10506.168 | 10544.52 | 10577.112 | 10653.144 | 10727.976 | 10846.488 | 10954.92 | 11113.32 | 11200.68 | 11254.68

## Slide 33: Annual Metered Water Consumption
Chart: million gallons per year
| 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 00 | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12
Residential | 2401.4832 | 2492.79 | 2583.3803 | 2289.0461 | 2144.6462 | 1831.8999 | 1744.048 | 1949.303 | 2043.1433 | 2155.5116 | 2192.8996 | 2314.4077 | 2453.3158 | 2243.3425 | 2345.9202 | 2341.8474 | 2345.2912 | 2338.9668 | 2313.5685 | 2335.6285 | 2222.0866 | 2111.34 | 2084.6723 | 2109.3 | 1904.135 | 1875.1971 | 1817.269 | 1878.4935
Business | 930.9361 | 908.6898 | 791.6174 | 742.8014 | 686.1471 | 669.0306 | 631.6897 | 659.7225 | 663.6914 | 663.2179 | 674.0408 | 715.0095 | 742.3309 | 680.9448 | 707.62 | 732.6727 | 716.7186 | 695.6774 | 665.9317 | 678.4001 | 671.0405 | 629.9476 | 635.907 | 609.6 | 553.805 | 527.2802 | 517.0094 | 547.0131
Industry/UCSC | 129.8483 | 126.3963 | 279.3331 | 260.9712 | 265.5243 | 264.7606 | 232.3019 | 299.6204 | 305.8437 | 297.8162 | 354.742 | 380.1665 | 432.3208 | 387.0354 | 408.4776 | 377.4588 | 341.925 | 232.6579 | 247.2462 | 248.6075 | 229.4931 | 235.7771 | 237.769 | 240.3 | 185.3589 | 227.4137 | 205.0388 | 225.0605
Irrigation | 301.082 | 290.0415 | 350.1575 | 315.1563 | 247.2723 | 224.3663 | 212.4791 | 236.469 | 205.1435 | 209.7594 | 212.5255 | 231.6511 | 289.3047 | 204.3095 | 237.5094 | 242.6961 | 281.2772 | 283.6 | 316.2551 | 329.9735 | 266.1406 | 276.9657 | 267.3913 | 282.9 | 199.71 | 194.3139 | 175.8638 | 221.4035
Municipal | 66.3334 | 68.9058 | 72.3144 | 53.3309 | 47.3738 | 48.6955 | 60.7436 | 79.8415 | 66.5959 | 79.0068 | 73.972 | 87.5265 | 98.9223 | 84.6549 | 60.5446 | 57.9678 | 69.0127 | 60.1 | 64.1672 | 63.2875 | 54.5112 | 53.4715 | 58.6193 | 65.7 | 46.2601 | 48.5175 | 42.7789 | 53.7797

## Slide 34: Metered Water Use by Customer Category

## Slide 35: Gallons per capita per day 2010 Urban Water Management Plan Figure 4-5 as augmented by additional data
Chart: Gallons per capita per day (GPCD)
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 est.
GPCD | 127 | 126 | 124 | 123 | 122 | 111 | 111 | 111 | 109 | 96 | 93 | 89 | 96 | 97
Residential GPCD | 80 | 80 | 80 | 79 | 79 | 75 | 72 | 70 | 71 | 63 | 62 | 59 | 61 | 62

## Slide 36: Average Per Capita Water Use 2001-2010
City of Santa Cruz today – 97 gpcd

## Slide 37: Customer Characteristics

## Slide 38: Customer Accounts Broken Down by Type and Geographic Area
Calendar Year 2013 |  |  |  |  | 
Customer Class | Inside City | Capitola | North Coast | Outside City | Total
Single family | 12,212 | 134 | 22 | 6,590 | 18,958
Multi-family | 1,788 | 5 | 8 | 930 | 2,731
Irrigation residence | 127 | 3 | - | 70 | 200
Irrigation business | 118 | 18 | - | 116 | 252
Bulk/Hydrant meters | 31 | - | - | 1 | 32
North Coast Irrigation | - | - | 28 | - | 28
Irrigation golf | 1 | - | - | 5 | 6
Construction | 64 | - | 1 | 3 | 68
Business general | 1,077 | 72 | 10 | 542 | 1,701
Business restaurant | 102 | 2 | - | 2 | 106
Hotel/motel | 79 | 2 | - | 4 | 85
Industrial | 31 | - | - | 7 | 38
UC Santa Cruz | 11 | - | - | - | 11
City of Santa Cruz | 210 | - | 3 | 5 | 218
Total | 15,851 | 236 | 72 | 8,275 | 24,434

## Slide 39: Water Consumption by Customer Class and Geographic Location
Calendar Year 2013 Figures are in millions of gallons |  |  |  |  | 
Customer Class | Inside City | Capitola | North Coast | Outside City | Total
Single family | 764 | 9 | 2 | 451 | 1,266
Multi-family | 366 | 4 | 2 | 319 | 690
Irrigation residence | 28 | <1 | - | 15 | 44
Irrigation business | 38 | 4 | - | 33 | 75
Bulk/Hydrant meters | 2 | - | - | - | 2
North Coast Irrigation | - | - | 24 | - | 24
Irrigation golf | 45 | - | - | 63 | 108
Construction | 1 | - | - | - | 1
Business general | 249 | 30 | 4 | 169 | 452
Business restaurant | 38 | 1 | - | 1 | 40
Hotel/motel | 70 | 8 | - | 2 | 80
Industrial | 55 | - | - | 1 | 56
UC Santa Cruz | 182 | - | - | - | 182
City of Santa Cruz | 61 | - | <1 | 1 | 62
Total | 1,899 | 56 | 32 | 1,055 | 3,043

## Slide 40: Indoor/Outdoor Breakdown (%)
Category | Indoor | Outdoor
Single Family | 77 | 23
Multi-family | 88 | 12
Business | 79 | 21
UCSC | 77 | 23
Municipal | 32 | 68
Irrigation | 0 | 100
Golf | 0 | 100

## Slide 41: End Use Breakdown Typical Single Family Account
Chart: Internal End Uses 153 gallons/household/day
| SF Toilets | SF Baths | SF Showers | SF Faucets | SF Dishwashers | SF Laundry | SF Other | SF Int. Leakage
Internal End Uses | 25.2511 | 3.8259 | 37.4941 | 30.6075 | 3.0607 | 24.486 | 20.66 | 7.6519
Chart: External End Uses 47 gallons/household/day
| SF Irrigation | SF Pools | SF Wash-Down | SF Car Washing | SF Ext. Leakage
External End Uses | 37.1657 | 0.46457 | 3.252 | 3.252 | 2.3

## Slide 42: Baseline Conservation Survey: Summary of Key Findings for Single Family Residential Accounts
Item | Standard | No. surveyed | Average per household | Percent water efficient
Faucets | 2.2 gpm | 352 | 3.5 | 83%
Showerheads | 2.5 gpm | 176 | 1.8 | 92%
Toilets | 1.6 gpf | 208 | 2.1 | 90%
Clothes Washers | Type | 96 | 0.96 | 62%
Dishwashers | Age | 81 | 0.81 | 65%

## Slide 43: Baseline Conservation Survey: Summary of Key Findings for Multi-Family Residential Accounts
Item | Standard | No. surveyed | Average per household | Percent water efficient
Faucets | 2.2 gpm | 322 | 2.4 | 87%
Showerheads | 2.5 gpm | 152 | 1.2 | 95%
Toilets | 1.6 gpf | 181 | 1.3 | 89%
Clothes Washers | Type | 44/109 | 0.4/0.08 | 58/46%
Dishwashers | Age | 49 | 0.4 | 45%

## Slide 44: Lot Characteristics
 | Single Family | Multi-Family | Commercial (includes Schools)
Mean Lot Size (sq. ft.) | 8,574 | ~50,000 | ~104,450
Median Lot Size (sq. ft.) | 6,316 | 9,600 | 14,810
Sites with Landscaping | 98% | 73% | 54%
Average Lot Area in Landscaping sq. ft. (%) | 1,884 (22%) | 5,800 (12%) | 4,835 (5%)
Sites with Turf | 48% | 51% | 15%
Average Turf Area (sq. ft.) | 542 | 2,744 | 3,005

## Slide 45: Irrigation Characteristics Types of Irrigation Equipment
Single Family Multi-Family Commercial

## Slide 46: Turf and Irrigation Characteristics Watering Turf with In-Ground Irrigation System
Single Family | Multi-Family | Commercial
62.5% | 71.2% | 74.4%

## Slide 47: Future Supply

## Slide 48: Supply Modeling
Confluence Model Inputs
  Hydrology
  Operating rule curves for various sources
  System demand – by customer class
  Water rights constraints
  Models aren’t static, as you learn more about the system and how the model forecasts it, questions and issues are identified that are researched and result in refining the model. This continuous “calibration” process is always a part of developing and using a supply model.

## Slide 49
Summary of Santa Cruz Confluence Assumption Changes over Time |  |  |  | 
Modeling Parameter | For IWP | Interim Assumption Adjustment (2010) | HCP (outdated) | Current/HCP
Annual Demand (mg) | 4,600 - 5,300 | 3,500 - 4,500 | 3,500 | 3,500 - 4,000
Demand Shape (Percent of annual demand in peak season) | 57% | 64% | 64% | 57%
Loch Lomond Rule Curves | Calibrated to 1977 | Calibrated to 1977 | Calibrated to 1977; then to 1990 | Calibrated to 1990
Loch Lomond Water Right | 1.043 billion gallon annual withdrawal limit | 1.043 billion gallon annual withdrawal limit | 1.043 billion gallon annual withdrawal limit | No Limit
N. Coast Annual Ad Demand (mg) | 30.8 | 30.8 | 81.4 | 22.5
Tait St. Diversion Capacity (cfs) | 11.52 | 11.52 | 11.52 | Peak: 12.2 Off-Peak: 11.52

## Slide 50: Forces Affecting Future Supply

## Slide 51: Fish Flow Releases
Sources of and rationale for selecting flow sets for use in Recon:
  Modeling changes are underway and are expected to be finalized by the fall;
  DEIR fish flow release flow sets have been presented to the public previously, so maintaining consistency with these flow sets seems to make sense, especially for use in Recon.

## Slide 52: Fish Flow Tiers – what do they mean? Tier 1, 2 and 3
Tier 1 refers to the (then) current voluntary flow releases initiated by the City in 2007 to maintain current habitat levels.
Tier 2 would limit City diversions & thereby increase baseflows in priority streams (Laguna Creek and the San Lorenzo River below Tait Street), as well as increase winter flows for adult migration and spawning in these streams.
Tier 3 would further limit City diversions to further increase baseflows in North Coast streams and the San Lorenzo River, providing 80 percent of optimum flows for fish habitat. Tier 3 leaves the most water in the streams for fish habitat, and results in the least amount of flowing water available for City diversion.

## Slide 53: Fish Flow Tiers – what do they mean? Tier 3/2
Tier 3/2 is a combination of tiers three and two. It is designed to maintain flows to maintain all life history stages of steelhead and coho and includes:
  Minimum in-stream flows to maintain all life history stages for coho salmon and steelhead;
  Bypass flows in wet and normal years to achieve habitat values for all life stages of steelhead and coho that are approximately 80 percent of the habitat value that would occur in the absence of the City diversions; and
  In dry and critically dry years, bypass flows are targeted to provide approximately 80 percent of habitat values that would occur in the absence of City diversion in Laguna and San Lorenzo River below Tait Street, while providing habitat values in the other streams that are improvements over existing operations, but do not fully achieve 80 percent of the habitat value.

## Slide 54: Monthly Source Production Under 1977 Hydrologic Conditions – Natural Flows (millions of gallons per month)
Chart: 
| Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
Beltz Wells | 4 | 0 | 0 | 0 | 0 | 0 | 24.8 | 33 | 34.1 | 34.1 | 24 | 24.8
North Coast | 61.3888 | 77.3173 | 71.7672 | 69.346 | 77.5342 | 72.2556 | 77.3939 | 73.1412 | 69.9574 | 66.9428 | 65.9596 | 74.6126
Tait Street | 122.6065 | 132.7501 | 114.5745 | 120.4102 | 127.6146 | 145.1035 | 230.8121 | 212.4031 | 170.0089 | 166.3591 | 183.9301 | 200.728
Loch Lomond | 29.3563 | 13.9896 | 37.2 | 12.4064 | 18.9255 | 0 | 8.016 | 42.3015 | 77.5012 | 77.2253 | 50.6367 | 16.7473
TOTAL DEMAND | 213.1004 | 218.0388 | 218.0388 | 196.7116 | 218.0388 | 211.7294 | 357.8933 | 398.1321 | 424.5825 | 417.9368 | 371.1474 | 352.9944

## Slide 55: Monthly Source Production Under 1977 Hydrologic Conditions – Tier 3/2 Flows (millions of gallons per month)
Chart: 
| Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
Beltz Wells | 9.2111 | 0 | 0 | 0 | 0 | 0 | 24.8 | 33 | 34.1 | 34.1 | 24 | 24.8
North Coast | 47.0378 | 53.9075 | 47.082 | 44.5262 | 47.7302 | 45.2023 | 55.8193 | 55.3701 | 56.494 | 52.8168 | 54.801 | 63.0043
Tait Street | 144.9072 | 154.2871 | 135.5573 | 142.4101 | 152.4395 | 169.9926 | 210.812 | 161.2389 | 109.9018 | 106.2519 | 131.2074 | 144.6286
Loch Lomond | 29.8474 | 13.9896 | 38.9277 | 13.2407 | 21.5203 | 0 | 18.6269 | 50.7054 | 75.8319 | 75.8513 | 54.7539 | 41.584
TOTAL DEMAND | 213.1004 | 218.0388 | 218.0388 | 196.7116 | 218.0388 | 211.7294 | 357.8933 | 398.1321 | 424.5825 | 417.9368 | 371.1474 | 352.9944

## Slide 56: Monthly Source Production Under 1977 Hydrologic Conditions – Tier 3 Flows (millions of gallons per month)
Chart: 
| Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
Beltz Wells | 24 | 0 | 0 | 0 | 0 | 24 | 24.8 | 33 | 34.1 | 34.1 | 24 | 24.8
North Coast | 22.717 | 23.867 | 15.9368 | 12.9474 | 12.1193 | 5.2147 | 7.4276 | 30.319 | 32.4512 | 28.8954 | 34.5548 | 35.9034
Tait Street | 98.1906 | 64.9862 | 98.0211 | 74.0534 | 104.7131 | 49.616 | 71.2623 | 54.2776 | 43.2665 | 48.2773 | 80.5362 | 77.202
Loch Lomond | 61.2498 | 130.9278 | 106.5737 | 111.426 | 106.8745 | 15.3153 | 25.4751 | 5.7408 | 0 | 0 | 0 | 0
TOTAL DEMAND | 213.1004 | 218.0388 | 218.0388 | 196.7116 | 218.0388 | 211.7294 | 357.8933 | 398.1321 | 424.5825 | 417.9368 | 371.1474 | 352.9944

## Slide 57: Fish Flow Tiers – what do they mean? DFG 5
DFG 5: is the CDFWs counter proposal to Tier 3/2 which includes a number of infrastructure improvements such as a second pipe between Felton diversion and Newell Creek Dam

## Slide 58
Tier 3:
As submitted to the resource agencies in August 2011 as part of a broader draft conservation strategy (which also included much lower flow goals known as Tiers 1 and 2), this flow strategy for North Coast and Tait St. sources includes:
Diversions would be limited to achieve approximately 80% of the habitat value in North Coast streams and the San Lorenzo River that would exist in the absence of City diversions.
Tier 3/2:
Upon receiving feedback that the August 2011 City proposal needed to be more responsive to several issues including dry year rearing flows and smolt outmigration, a hybrid Tier 3/2 flow proposal was developed and submitted to the resource agencies in July 2012. This includes the following flow goals for the North Coast and Tait St. sources:
Under this hybrid scenario, Laguna Creek and the San Lorenzo River would receive Tier 3 flows in normal and wet years and Tier 2 flows in drier years with a small number of “exception” years where a minimal flow (aka “Tier 1”) would be provided in extreme drought conditions. Tier 2 flows generally include lower flows for smolt outmigration and rearing than does Tier 3, while Tier I flows have minimal flows to support only rearing in all streams.
DFG 5:
In response to the City’s July 2012 proposal, the Department of Fish and Wildlife (then DFG) submitted a counterproposal in September 2012. This proposal included the following modifications of the City’s July 2012 proposal for North Coast and Tait St. sources:
Criteria for determining “exception years” (and subsequently reduced flow goals) based on reservoir storage levels.
Lower adult migration flow triggers
Increased smolt outmigration flows
Generally higher rearing flows
Reduced adult migration, spawning and incubation flows in Liddell and Majors Creeks in dry years

## Slide 59: Climate Change

## Slide 61: Potential Implications of Climate Change for Santa Cruz’s Water Supply
Probable increased variability overall,
Probable increased frequency of drought, and
Probable changes in precipitation patterns

## Slide 62: Implications of Potential Source of Supply Changes on Source Characteristics

## Slide 63
Watershed Impacts on Water Quality:
Coliform/Bacteria
TOC TTHM
Sludge Processing
Sand Removal

## Slide 66
Beltz Wells
4%
Tait Wells
3%
Loch
Lomond
22%
San Lorenzo
River
46%
North Coast
Streams
25%
North Coast Streams (1890)
Loch Lomond Reservoir (1960)
San Lorenzo River (1924)
Beltz Wells (1964)
Water Sources
TOC: 4-6 mg/L
TOC: 0 mg/L
TOC: <1mg/L
TOC: 2-4 mg/L
( >10 During High Flows)

## Slide 67: THM Source Formation Potentials
Chart: 
 | 1077 | 2008 | 1042 | 187
Chart: 
 | 1077 | 2008 | 1042 | 187
24%
47%
TTHM’s
140 ppb
TTHM’s
70 ppb
MCL
80 ppb
25%
River/Stream
Reservoir

## Slide 68
GHWTP sludge discharge to the sanitary sewer

## Slide 69: Future Demand

## Slide 70: How We Estimate Demand Major Inputs, Methodologies, and Source Reference
Major inputs:
  Population forecasts (AMBAG)
  Growth in number of accounts for each class of customers (calculated based on population)
  Water use in future development (developed based on recent actual experience)
Selected methodology comes from the AWWA M50 Manual: Water Resources Planning
Price hasn’t been formally factored into projections but obviously has an impact and needs to be considered.

## Slide 71: 2010 Urban Water Management Plan Demand Forecasts*
Used population forecasts created by the Association of Monterey Bay Area Governments
Were created using one method for customers inside Santa Cruz and another for those living outside Santa Cruz
The inside Santa Cruz forecast was developed to align with the Santa Cruz 2030 General Plan
Included 2 scenarios – Scenario 1 based on higher per account water use levels during 1999 to 2004, and Scenario 2 based on the lower per account water use levels occurring during 2007 and 2008
* For a more detailed description of the methodology, please see http://www.cityofsantacruz.com/Modules/ShowDocument.aspx?documentid=24687

## Slide 72: Demand Projection from the 2010 Urban Water Management Plan Water Demand Forecast Scenario 2, Table 4-11
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2015 | 2020 | 2025 | 2030
Gross Annual Water Use per Calendar Year | 3.987 | 3.962 | 3.909 | 3.898 | 3.895 | 3.567 | 3.57 | 3.59 | 3.565 | 3.212 | 3.192 | 3.067 | 3.295 | 3.477 | 3.684 | 3.847 | 3.946 | 4.046

## Slide 73
Location: | Customer Class | 2010 | 2015 | 2020 | 2025 | 2030 | 
City of Santa Cruz | Single Residential | 839 | 854 | 869 | 884 | 899 | 
 | Multiple Residential | 408 | 424 | 440 | 456 | 472 | 
 | Business/Industry | 425 | 454 | 483 | 511 | 540 | 
 | Municipal | 54 | 54 | 55 | 55 | 56 | 
 | Irrigation/Golf | 115 | 118 | 120 | 122 | 125 | 
 | UC Santa Cruz | 212 | 276 | 339 | 344 | 349 | 
Inside City Subtotal (millions of gallons) |  | 2,055 | 2,180 | 2,306 | 2,373 | 2,441 | 
Outside City: County, Capitola, & North Coast Irrigation | Single Residential | 502 | 513 | 523 | 533 | 543 | 
 | Multiple Residential | 336 | 343 | 350 | 357 | 364 | 
 | Business/Industry | 231 | 236 | 240 | 245 | 250 | 
 | Municipal | - | - | - | - | - | 
 | Irrigation/Golf | 130 | 133 | 135 | 138 | 141 | 
Outside City Subtotal (millions of gallons) |  | 1,199 | 1,224 | 1,248 | 1,273 | 1,297 | 
Other miscellaneous uses including water losses |  | 268 | 280 | 292 | 300 | 307 | 
Total System Water Demand (millions of gallons) |  | 3,522 | 3,684 | 3,847 | 3,946 | 4,046 | 
Notes: |  |  |  |  |  |  | 
(a) Assumes existing (2010) water demands recover to 2007-08 levels |  |  |  |  |  |  | 
2010 Urban Water Management Plan Table 4-11: Water Demand Forecast, Scenario 2 (a)

## Slide 74: Price Elasticity of Demand*
Measures the responsiveness of the quantity of water demanded to a change in price;
For example, a 15% rate increase with a -0.3 elasticity would result in a 4.5% reduction in demand;
Measured price elasticities of demand between 0 and -1 are referred to as “relatively” inelastic because the percentage change in quantity is less than the percentage change in price.
* From Forecasting Urban Water Demand, R. Bruce Billings and Clive V. Jones; Second Edition, AWWA 2008

## Slide 75
Price Elasticity of Water Demand – Elasticity Factors |  | 
 | Marginal Price in Rate Structure | 
 | Uniform Rates | Increasing Block Rates
Base case elasticity | -0.4 | -0.5
Additions or Subtractions |  | 
Marginal price on bills | -0.1 | -0.15
Wet/cold climate | +0.1 | +0.1
Arid West | -0.1 | -0.1
Winter (low irrigation season) | +0.15 | +0.15
Summer (high irrigation season) | -0.15 | -0.15
Bills > 1.5% of average income | -0.1 | -0.1
Bills < 0.5% of average income | +0.2 | +0.2
Effective Long Term Conservation | +0.1 | +0.1
Adapted from Table 9-5, Second Edition, Forecasting Urban Water Demand, R. Bruce Billings and Clive V. Jones, AWWA 2008

## Slide 76: Santa Cruz’s Current Water Rates: Fixed Water Rate Charges Based on Meter Size and Volume Rates for SFR and Duplex Customers
Meter Size | Inside City (Monthly) | Outside City (Monthly)
5/8" and 3/4" | $17.41 | $22.20
1” | 43.52 | 55.50
1-1/2” | 87.05 | 110.98
2” | 139.27 | 177.57
3” | 261.14 | 332.95
4” | 435.23 | 554.92
6” | 870.46 | 1,109.83
8” | 2,002.05 | 2,553.34
10" | 2,472.09 | 3,151.92
Single-Family and Duplex Residential Customers |  | 
Units per billing period | Inside-City | Outside-City
1-4 ccf | $1.57 | $2.00
5-9 ccf | 4 | 5.1
10-14 ccf | 5.14 | 6.55
15-18 ccf | 7.05 | 8.98
Over 18 ccf | 8.79 | 11.21
Note: All other customers pay a uniform rate of $4 per ccf inside the city or $5.10 per ccf outside the city

## Slide 77: Price Elasticity for Santa Cruz
Using the elasticity factors from the elasticity table, single family/duplex residential elasticity would be:
  Summer elasticity (with long term conservation): -0.55
  Winter elasticity (with long term conservation): -0.25
Using the elasticity factors from the previous slide, elasticity for all other customers would be:
  Summer elasticity (with long term conservation): -0.45
  Winter elasticity (with long term conservation): -0.15

## Slide 78: If price were the only factor… what does history tell us about the potential elasticity of demand in Santa Cruz?
Between 2004 and 2008, demand, as measured by gross production, fell by 9%;
Between 2004 and the end of 2008 a series of rate increase totaling 82.5% was implemented (June 2004: 25%, January 2005 through 2008 20%, 15%, 12.5% and 10% respectively);
Actual rates for this period more than doubled (113.5%) due to compounding;
If no other variables, such as weather, influenced demand, and demand changed only due to price, the elasticity of demand for this period would be -0.11 for an 82.5% rate increase or -0.08% for the 113.5% rate increase

## Slide 79: Long Term Water Conservation Master Plan
Note: The Long Term Conservation Master Plan described in this presentation is a work in progress. Several slides in this part of the presentation show analytical results that are based on certain assumptions that may change over time. The purpose of including these slides is to demonstrate the analytical approaches that can be used in considering additional conservation measures rather than present final analyses and/or recommendations.

## Slide 80: How efficient are fixtures in the residential, commercial, and landscape sectors?
Preliminary Results Water Use Baseline Survey |  | 
 | SFR | MFR
Toilets | 90% | 91%
Showerheads | 92% | 98%
Bathroom Faucets | 90% | 82%
Kitchen Faucets | 71% | 82%
Clothes Washers | 63% | 46%
Notes: Toby
MFR – in-unit versus and common area laundries (separate data). >50% in common area machines were HECW
Future discussion on Saturation Study – HECW in unit efficiency ratings.

## Slide 81: Conservation Measure Screening
All Potential Measures Identified
Staff, Public, Consultant, and
Water Commission Input
90+ Measures Identified
39 Feasible Measures Remain
Measures Evaluated in the DSS Model
Measures Screened
Staff and Consultants Screen Measures with Decision Criteria
Notes: Flow of information

## Slide 83: Water Conservation Measures

## Slide 84: Projected Water Savings

## Slide 85: To assist in program evaluation, four conservation program plans were developed
Education and Mandates will be included in the Plan
Focusing on what levels of additional conservation measures are worth investing in for the next 10-20 years?
  Program A – “Current Program”
  Program B – “Customer Service & Cost Effective”
  Program C – “Optimized to Maximize Savings”
  Program D – “All Measures” (without exceeding saturation)

## Slide 87: Water Demands with Conservation Savings Projections

## Slide 88: Per Capita Water Use with Conservation Savings Projections

## Slide 89: Comparison of Programs

## Slide 92: Program B vs. C Program Implementation Costs
Notes: TOBY

## Slide 93: Conclusion and Take Aways

## Slide 94: Conclusion and Take Aways
Lots of opportunity to discuss and disagree about what are the right assumptions about future demand, but there is no guaranteed right answer;
Climate change introduces irreducible uncertainty into our process – ultimately we’ll have to figure out how to take this uncertainty into account in our planning, but we aren’t likely to find ways to resolve it; and
Scenario planning is a useful way to learn about and get a better handle on how the various factors we’re dealing with in our planning could affect our future.

## Slide 95: The End
(Thank Heavens!)